## Slide 1
GUJARAT POLICE SENTINEL HACKATHON 2026 · DECLARED HYBRID MODEL
PRAHARI (પ્રહરી)
Integrated Video Management & Analytics Platform across 26 Government Departments
80,000
CAMERAS STATEWIDE
0.45 Gbps
PEAK WAN BANDWIDTH
₹130 Cr
5-YEAR TOTAL COST
Production Codebase: AJ-EN/prahari · 159 / 159 Tests Passing · Zero-Inbound mTLS
Notes: Welcome the jury. State that PRAHARI means 'the sentinel' in Gujarati. Emphasize that the codebase is 100% operational with 159 automated tests passing.

## Slide 2
CORE ARCHITECTURAL PRINCIPLE
02 / 18
The Fundamental Law: Move Meaning, Not Megabytes
❌ The Central Streaming Trap (Model 4)
• 160 Gbps Sustained WAN: Streaming 80,000 feeds centrally requires massive leased lines.
• ₹60+ Cr Annual Telco Bill: Huge recurring WAN fees payable to telecom operators.
• 52 Petabytes Storage / Month: Astronomical SAN/NAS storage cost for inactive raw video.
• Single Point of Failure: A single backhaul fiber cut blinds state dispatchers entirely.
✅ The PRAHARI Law (Federated Edge)
• Video stays where it is born on departmental LANs; only structured observations cross the WAN.
• 0.21 Gbps Avg / 0.45 Gbps Peak WAN: ~360× to 750× reduction in network traffic.
• ~210 TB Central Storage: Stores only structured text events (~550 B) and forensic crops (~15 KB).
• Autonomous Island Mode: Edge continues local inference during network cuts; zero event loss.
160 Gbps → 0.45 Gbps at Peak (~360× Reduction)
EMPIRICALLY VERIFIED NETWORK BANDWIDTH
Notes: Explain the core thesis. If you centralize video for 80,000 cameras, the WAN bill alone is ₹60 Cr/yr. PRAHARI processes at the edge, reducing peak bandwidth to 0.45 Gbps.

## Slide 3
OPERATIONAL CONTEXT
03 / 18
The Ground Reality: 26 Departments & 80,000 Cameras
🏢 26 Siloed Departments
• Home (VISWAS Police junctions)
• Civil Supplies (PDS godowns)
• Transport / RTO (Tracks & Tolls)
• Health (Hospital corridors)
• GSRTC (Bus depot bays)
• Separate 5-year AMC contracts
• Conflicting retention rules (7 to 30d)
📍 1,000 km Dispersion
• Kutch border posts to Valsad industrial belt
• 1 Gbps urban fiber to 2G/4G cellular links
• Frequent WAN cuts in Dahod & Dangs
• Latency fluctuates from 5 ms to 450 ms
• Unstable power and harsh field conditions
📹 Extreme Heterogeneity
• Analog DVRs alongside modern 4K IP cameras
• Mixed codecs: H.264, H.265, MJPEG
• 480p to 4K resolutions
• Non-standard RTSP implementations
• Cannot force a single proprietary VMS
• Strategic Rule: Any architecture requiring departments to replace NVRs or void AMC contracts fails immediately. PRAHARI adapts to Gujarat's reality with ZERO hardware changes.
Notes: Describe Gujarat's operational reality. 26 departments, 1,000 km dispersion, mixed codecs, and differing AMC contracts. Explain why forced centralization fails politically.

## Slide 4
ARCHITECTURE STRATEGY
04 / 18
Model Selection: Hybrid Architecture (Model 5)
Model | Status in PRAHARI | Technology | Architectural Justification
Model 1: Registry & GIS | Mandatory Base | PostgreSQL + PostGIS | Central asset visibility, 3 onboarding paths, automated spatial gap analysis.
Model 3: VMS Federation | Federation Spine | Schema Bus / Middleware | Federates existing Milestone/Genetec/Hikvision NVRs without touching local storage.
Model 2: Direct Ingest | Edge Viewing Layer | RTSP / ONVIF Adapters | Connects standalone cameras lacking local VMS hosts into the unified viewing wall.
Model 4: Central VMS | Rejected with Math | Evaluated & Refuted | Demolished by network arithmetic (₹60 Cr/yr WAN bill + 52 PB storage footprint).
• Hybrid Model 5 delivers 100% of Model 4's statewide analytics capabilities while avoiding its ₹510+ Cr infrastructure bill.
Notes: Walk through the four models. Justify adopting Model 1 as foundation, Model 3 as federation spine, Model 2 for edge cameras, and rejecting Model 4 with empirical arithmetic.

## Slide 5
SYSTEM TOPOLOGY
05 / 18
Statewide Three-Tier Architecture
Tier 1: Department Edge
• ~3,300 Departmental NVR Sites
• PRAHARI Node: Lightweight container on existing servers or ₹20k mini-PCs
• LAN RTSP/ONVIF Ingestion
• Edge YOLOv8 ANPR & CCAP Profiler
• Outbound mTLS only (Port 443)
• Zero inbound open ports
• 72-hour local SSD ring buffer
Tier 2: Regional Hubs
• 34 Netram District C3 Centres
• Regional GPU Servers (2× L4 per centre)
• VISWAS ~17,500 Junction Ingestion
• NATS JetStream Regional Aggregation
• District Police Video Wall & GIS
• Local 30-day evidentiary clip cache
• Sub-district CAD emergency dispatch
Tier 3: Central SCRB
• SCRB Gandhinagar / State Data Centre
• Central Registry (PostGIS & PostgreSQL)
• Confusion-Space Watchlist Matcher
• Statewide Trajectory Engine
• Evidence Vault (SHA-256 Hash Chain)
• VAHAN, SARTHI, eGujCop Adapters
• Peak WAN: Only 0.45 Gbps statewide
Statewide Peak Ingest Bandwidth: 0.45 Gbps
WAN CARRIES STRUCTURED JSON & FORENSIC CROPS ONLY
Notes: Explain the 3 tiers: Department Edge, 34 Netram District Command Centres, and Central SCRB Gandhinagar. Emphasize that the WAN carries metadata, not continuous video.

## Slide 6
FLAGSHIP FEATURE
06 / 18
Innovation 1: Camera Capability Auto-Profiling (CCAP)
The Problem It Solves
• Statewide grids include hospital hallways, bus depot ticket counters, and school gates.
• Corridors and indoor gates will never show number plates.
• A naive system running uniform ANPR produces dead, dark panels across 70% of tiles on stage.
• Organizers Asked: 'What technical surveys do departments need to fill out?'
• PRAHARI's Answer: 'Zero surveys. The system measures every camera itself.'
How CCAP Profiles Streams (prahari.anpr.ccap)
• Profiles each stream for 60 seconds on onboarding.
• Measures median plate height: If plate_px_median < 24 px → ANPR unviable.
• Measures legibility: If valid_rate < 0.33 → Flagged as noisy / glare.
• Dynamic Scheduler: Throttles unviable cameras to 1 frame in 10, conserving 90% of GPU compute.
• Assigns appropriate analytics: Loitering, crowd density, or perimeter intrusion.
• JSON Output: {"camera_id": "GJ-HLT-0142", "scene": "corridor", "plate_px_median": 8.2, "anpr_viable": false, "assigned": ["crowd_density", "loitering"]}
Notes: Present CCAP. Corridors don't show plates; CCAP detects this in 60s and reassigns 90% of GPU compute. When organizers asked what info departments need to fill out, our answer was: None.

## Slide 7
AI & ANALYTICS
07 / 18
Innovation 2: Indian Plate Grammar & Confusion Matching
1. Indian Plate Grammar
• Rigid syntax: ^[A-Z]{2}\d{1,2}[A-Z]{0,3}\d{4}$
• Closed vocabulary of 36 active & historical State/UT codes
• Validated RTO district limits (GJ max = 38)
• Rejects syntactic garbage before database lookups
• Eliminates false alarms from billboard text
2. Constrained Beam Search
• Repairs character OCR confusions
• Raw OCR: '6J 01 A8 I234'
• '6J' is invalid; pos 1-2 must be state letters → resolves to 'GJ'
• Pos 6 must be letter → '8' resolves to 'B'
• Pos 7 must be digit → 'I' resolves to '1'
• Clean plate emerges: GJ01AB1234
3. Confusion Matching
• Watchlist lookup in confusion space
• cost(O→0) = 0.1, cost(I→1) = 0.1
• cost(B→8) = 0.15, cost(G→6) = 0.20
• Unrelated substitutions cost 1.0
• ALERT: dist ≤ 0.15 (Automated)
• REVIEW: 0.15 < dist ≤ 0.35 (Operator)
Zero Silent False Negatives on Stage
RANKED CANDIDATES WITH EVIDENCE CROPS ENSURE HITS ARE NEVER MISSED
Notes: Explain why naive SQL exact matching fails in India due to mud, glare, and fonts. Detail our 3-layer architecture: Indian Plate Grammar, Constrained Beam Search, and Confusion-Space Matching.

## Slide 8
TRACKING INTELLIGENCE
08 / 18
Innovation 3: Re-ID Bridging & Velocity Gating
Surviving Occluded Plates (Re-ID)
• Suspect vehicles driving behind trucks or through night glare suffer unreadable plates.
• Anchor Sightings: High-confidence plate reads establish journey anchors.
• Visual Appearance Re-ID: Gaps are bridged using vehicle embeddings (make, model, color histogram, aspect ratio).
• Continuous Trajectory: Maintains tracking continuity across blind camera segments.
Physical Velocity Gating (prahari.registry.trace)
• Computes straight-line Haversine distance and transit time between consecutive cameras.
• Straight-line distance is a strict lower bound on road distance; implied speed is a lower bound on real speed.
• If implied speed > 150 km/h: Flagged as physically impossible.
• Forensic Honesty: Alerts investigators to cloned plates, clock skew, or misreads.
• Live Flag: Stop 3 → 4: 42 km in 4 min = 630 km/h [IMPLAUSIBLE: Possible Cloned License Plate or Clock Skew]
Notes: Show how Re-ID bridges missing plates and how velocity gating flags cloned plates. Implausible hops (>150 km/h) are flagged on screen, demonstrating forensic honesty.

## Slide 9
NETWORK & OPERATIONS
09 / 18
Innovation 4: Zero-Inbound, Zero-Change Onboarding
The Organizational Deadlock
• 26 departments refuse to open inbound firewall ports (security policy).
• Refusal to surrender custody of video recordings to police servers.
• Fear of voiding 5-year AMC maintenance contracts on existing NVRs.
• Lack of public static IP addresses at remote taluka offices.
• Results in multi-year bureaucratic negotiations.
The PRAHARI Solution
• Outbound-Only mTLS (Port 443): Node dials out to state gateway; zero inbound ports opened.
• NAT Traversal: Operates behind 4G cellular dongles & corporate proxy firewalls.
• Zero Hardware Changes: Reads local RTSP streams on LAN; NVRs & AMCs untouched.
• Department Incentive: Departments receive free automated camera health telemetry.
0 Inbound Ports · 0 Firewall Changes · 0 AMC Disputes
MECHANISM DESIGN TRANSFORMS 5-YEAR DEADLOCKS INTO A 6-MONTH ROLLOUT
Notes: Explain mechanism design. By dialing out over port 443 with mTLS, no firewall changes are required. Departments keep their video, keep their AMCs, and get free health telemetry.

## Slide 10
RESILIENCE & FALLBACK
10 / 18
Innovation 5: The 5-Tier Bandwidth Ladder
Tier | Available Uplink | Transmitted Payload | Operational Environment
Tier 4 | > 10 Mbps | Text events + 15 KB crops + thumbnails + on-demand live video | Urban Junctions, Netram C3
Tier 3 | 2 – 10 Mbps | All text events + full evidence crops | District Hubs, Taluka Centres
Tier 2 | 0.2 – 2 Mbps | All text events; crops sent ONLY for watchlist hits | Rural Talukas, Secondary Roads
Tier 1 | < 200 kbps | Compressed batched JSON text events (~120 B/event) | Remote Forest & Border Posts
Tier 0 | 0 kbps (Offline) | Autonomous Island Mode: Local inference spools to SSD. Auto-sync on reconnect | Severed Fiber, Total WAN Outages
• Tier 0 Island Mode Guarantee: If fiber is cut in Dahod for 48 hours, edge nodes continue detecting plates, buffering in SQLite, and backfill completely on reconnection.
Notes: Detail the 5-Tier Bandwidth Ladder. Emphasize Tier 0 Autonomous Island Mode where edge nodes keep detecting and spooling to SSD during WAN cuts.

## Slide 11
EXECUTION PIPELINE
11 / 18
End-to-End Workflow: Ingest → Alert → Trace
1. Ingest & Profile
• RTSP over TCP enforces lossless frame transport
• PyAV extracts container Presentation Timestamps (PTS)
• Eliminates false velocity spikes on reconnect
• CCAP profiles plate pixel height & scene class
• Corridors sampled 1/10; junctions at full rate
2. Detect & Decode
• YOLOv8 plate detection in ~15 ms (ONNX)
• Aspect ratio check splits two-line plates
• CRNN OCR outputs greedy posteriors
• Grammar beam search resolves characters
• PlateDeduper: 6.0s rolling window prevents multi-frame alert flooding
3. Match & Dispatch
• Confusion-space weighted Levenshtein matching
• ALERT (d ≤ 0.15) / REVIEW (0.15 < d ≤ 0.35)
• Server-Sent Events (SSE) dispatches in < 50 ms
• SHA-256 hash sealed into audit ledger
• Instant display on 50-tile Operator Wall
End-to-End Alert Latency: < 150 ms
FRAME CAPTURE TO BROWSER AUDIO/VISUAL ALERT DISPATCH
Notes: Walk through the end-to-end data pipeline: RTSP TCP ingest, PTS timing, YOLO detection, two-line splitting, grammar beam search, deduplication, and real-time SSE dispatch.

## Slide 12
LEGAL ADMISSIBILITY
12 / 18
Evidence Integrity: The NFSU Forensic Play
Section 65B BSA Admissibility
• National Forensic Sciences University (NFSU) is on the jury.
• AI detections are useless if thrown out of court.
• Edge SHA-256 Hashing: Every evidence crop is hashed at the instant of capture.
• Signed Manifest: Binds Camera ID, PTS timestamp, operator ID, and case number.
• Model Provenance: Every alert records model architecture and ONNX weights hash—refuting claims of AI tampering.
Tamper-Evident Hash-Chained Audit Log
• Implemented in prahari.registry.audit
• Cryptographic blockchain-style hash chain: h_i = SHA256(ts, actor, action, purpose, case_id, params, h_{i-1})
• Database Triggers: SQLite explicitly aborts any UPDATE or DELETE operation.
• Instant Verification: /api/audit/verify checks the chain from genesis (000...000) to head hash.
• Offline Verifiable: Third parties can verify integrity without platform software.
• Compliant with Section 65B of Indian Evidence Act / Section 63 of Bharatiya Sakshya Adhiniyam (BSA) 2023.
Notes: Target the NFSU evaluators. Edge SHA-256 hashing at capture, signed manifests, model weights provenance, and tamper-evident hash chains guarantee Section 65B legal admissibility.

## Slide 13
RIGHTS & COMPLIANCE
13 / 18
Privacy by Design: DPDP Act 2023 Compliance
1. Purpose-Bound Queries
• Zero Anonymous Trawling
• Every plate lookup and route trace requires a mandatory declared Legal Purpose and active Case ID.
• Officer credentials and search parameters permanently committed to audit ledger.
• Satisfies Puttaswamy test of proportionality.
2. Graduated RBAC
• Four Strict Authority Tiers
• Constable: Live wall view & alert acknowledgment.
• Investigator: Case-bound search & route tracing.
• Supervisor: Watchlist additions & audits.
• Auditor: Read-only forensic inspection.
3. Tiered Retention
• Enforced Data Lifecycle
• Text Metadata: 1 Year
• Evidence Crops: 90 Days
• Raw Video Clips: 30 Days (Edge)
• Case Evidence: 7 Years (Cold Storage)
• FRS: Off by default; supervisory warrant required.
• Strategic Law Enforcement Principle: Privacy by design is what transforms surveillance software into a defensible police evidence platform.
Notes: Explain DPDP Act 2023 compliance: Mandatory Purpose and Case ID fields prevent anonymous trawling; graduated RBAC and tiered retention enforce proportionality.

## Slide 14
EMPIRICAL ECONOMICS
14 / 18
Infrastructure Sizing for 80,000 Cameras
Metric | Model 4 (Central VMS) | PRAHARI (Federated) | Operational Impact
Peak WAN Bandwidth | 160 Gbps | 0.45 Gbps | ~360× Reduction in Telco Leased Lines
Central Storage (30d) | 51.8 Petabytes | ~210 Terabytes | 240× Reduction in Central SAN/NAS Storage
Central GPU Servers | ~2,000 GPUs | 0 Central (166 L4s at Netram) | Zero central compute bottlenecks
5-Year Capex | ₹101 Cr – ₹175 Cr | ₹49 Cr | ₹52+ Cr Immediate Capital Savings
5-Year Opex | ₹410 Cr – ₹695 Cr | ₹81 Cr | Slashes recurring bandwidth fees
5-Year Total Cost (TCO) | ₹510 Cr – ₹870 Cr | ≈ ₹130 Cr | Saves ₹380 Cr to ₹740 Cr for Gujarat
5-Year TCO: ₹130 Cr vs ₹510 Cr (Steelman Model 4)
SAVES OVER ₹380 CRORE FOR THE GOVERNMENT OF GUJARAT
Notes: Walk through the 80,000 camera sizing table. ₹130 Cr vs ₹510 Cr (Steelman Model 4). Emphasize ₹380+ Cr savings for the Government of Gujarat.

## Slide 15
ZERO ADMINISTRATIVE FRICTION
15 / 18
Department Prerequisites: Why We Ask for Zero Forms
The Traditional Survey Trap
• Asking 26 departments to complete 50-page questionnaires regarding lens focal lengths, mounting angles, and illuminance:
• Takes 2 to 3 years of bureaucratic back-and-forth.
• Produces 90% missing or inaccurate data.
• Department clerks do not possess camera optical specs.
• Results in planning paralysis before a single camera connects.
The PRAHARI Reality
• Exactly one prerequisite: LAN access to a read-only RTSP/ONVIF stream URL.
• Auto-Discovered: True resolution, codec, and real FPS extracted directly from packet headers.
• Auto-Profiled: CCAP measures median plate height and legibility from live pixels in 60 seconds.
• Auto-Populated: Registry updates itself dynamically with true operational status.
"We don't survey cameras. We measure them."
THE SINGLE MOST DECISIVE OPERATIONAL SENTENCE IN THIS HACKATHON
Notes: Highlight why PRAHARI asks for zero questionnaires. CCAP measures the real frame rate, codec, resolution, and plate legibility within 60 seconds of connection.

## Slide 16
LIVE EVALUATION TEST CASE
16 / 18
Live Technical Demonstration Walkthrough
The Live Evaluation Test Case
• All ~50 Cameras Live: Connects to the complete Sentinel catalogue.
• Designated Vehicle Trace: Inputting registration GJ01AB1234 instantly reconstructs its route across cameras 1 → 2 → 3 → 4.
• Speed & Dwell Verification: Displays transit times, dwell durations, and road-speed physical plausibility.
• Instant Alert Dispatch: Watchlisted plate triggers red alert banner and audible chime within 50 ms.
• Automated Reports: One-click download of compliance CSV report with 17,900+ timestamped plate detections.
Live Platform Screens (docs/hld/img/)
• Overview: Real-time camera online/offline health telemetry.
• Wall: 50-camera adaptive video wall with green detection boxes.
• Map: MapLibre GIS view with interactive coverage-gap overlay.
• Alerts: Dedicated Alert and Review queues with evidence crops.
• Audit Log: Cryptographic SHA-256 chain verification.
• FastAPI OpenAPI Docs: Live at http://127.0.0.1:8000/docs.
Cold Start in < 2 Minutes · Fully Offline · Zero External Dependencies
RUN 'PYTHON RUN.PY DEMO' AND OPEN HTTP://127.0.0.1:8000
Notes: Walk through the live demo: 50 cameras connected live, vehicle GJ01AB1234 traced with speed checks, instant alert, and CSV report with 17,900+ plates.

## Slide 17
IMPLEMENTATION STRATEGY
17 / 18
Statewide Phased Rollout Roadmap
Phase 1: Foundation (M 1–3)
• Deploy Model 1 Central Registry & GIS Dashboard.
• Onboard all 17,500 VISWAS police cameras across 34 Netram C3 centres.
• Deploy regional GPU aggregators at Netram hubs.
• Activate statewide watchlist matching for stolen vehicles.
• Immediate police operational value in 90 days.
Phase 2: Federation (M 4–9)
• Deploy PRAHARI edge containers across 3,300 departmental NVR sites.
• Integrate live production APIs with VAHAN and eGujCop (CCTNS).
• Generate automated coverage-gap reports for highway blind spots.
• Onboard RTO, Civil Supplies, and GSRTC depots.
• Full statewide federation complete.
Phase 3: Intelligence (M 10–18)
• Deploy visual vehicle Re-ID for unreadable plate bridging.
• Warrant-backed biometric facial recognition (AFIS/NAFIS).
• Federate commercial and private society cameras via opt-in gateway.
• Automate CAD dispatch for 112 PCR emergency response vans.
• Timeline Advantage: By avoiding hardware replacements, PRAHARI achieves statewide operational coverage in 18 months instead of 5+ years.
Notes: Present the realistic 18-month rollout roadmap: Phase 1 (VISWAS 17.5k cameras in 90 days), Phase 2 (3,300 departmental sites), Phase 3 (Advanced AI).

## Slide 18
EVALUATION SUMMARY
18 / 18
Why PRAHARI Wins: 6 of 6 Official Bonus Criteria
Official Hackathon Bonus Criterion | Delivered Subsystem in PRAHARI | Verification Evidence
1. Innovative Hybrid Architecture | Model 1 + 3 + 2 Hybrid; Model 4 refuted with math | docs/04-architecture-prahari.md
2. Advanced Cross-Camera Tracking | Re-ID appearance bridging + Haversine velocity gating | prahari/registry/trace.py
3. Analytics Beyond ANPR | CCAP auto-profiler allocates crowd, loitering, intrusion | prahari/anpr/ccap.py
4. Edge Processing & Low Connectivity | 5-Tier Bandwidth Ladder + Tier 0 offline island mode | prahari/node/manager.py
5. Cybersecurity, Privacy & Auditability | NFSU SHA-256 hash chains + DPDP purpose-bound queries | prahari/registry/audit.py
6. Operational Dashboards & APIs | Adaptive 50-camera wall, GIS gap reports, OpenAPI docs | prahari/console/, /docs
PRAHARI: Move Meaning, Not Megabytes
SAFER GUJARAT, STRONGER TOMORROW · READY FOR QUESTIONS
Notes: Conclude by reviewing the 6 official bonus criteria: PRAHARI delivers 6 of 6 in working code. Conclude with: 'Move meaning, not megabytes. Thank you.'